## Slide 1: Unit 4, Lesson 9 Connecting a Windows XP Peer-to-Peer Network
AOIT
Computer Networking
Copyright © 2008–2012 National Academy Foundation. All rights reserved.
Notes: This presentation is a teacher resource that provides you with step-by-step instructions for setting up a peer-to-peer network between two computers running Windows XP.

## Slide 2: Use UTP cable to physically connect the computers
Connect computers directly with UTP cable or thinnet cable.
Green lights indicate the hardware is functioning correctly.
Notes: To set up the hardware connection for a peer-to-peer network, run UTP or thinnet cable from one computer to the other. No router is needed. If you are connecting more than two computers, you will need a T-connector or a hub.
When the connection is working, both computers will display a green light next to the cable connection, as indicated in the pictures.
In this example, a laptop is connected to a desktop using a UTP cable. Both computers have Windows XP operating systems. To establish your peer-to-peer network, you will need to go through the entire setup process on both computers. You can go through the entire process outlined in this presentation for one computer, and then for the other computer.

## Slide 3: Use the ping command to check the connection
    Select Run from the Start menu and enter cmd.
    Type ping 127.0.0.1 at the command prompt.
You can ping your own computer to check that the hardware connection is functioning properly:
Notes: When you ping your own computer, the operating system will provide you with information about packets sent and received, and the round-trip time. This verifies that the hardware connection is able to send and receive data.

## Slide 4: Set up local area connection properties
In the Local Area Connection Properties dialog box, check the following boxes:
Client for Microsoft Networks
File and Printer Sharing
TCP/IP
Notes: If the hardware is functioning correctly, the next step is to make sure everything is in place to make the software connections. The checkboxes Client for Microsoft Networks, File and Printer Sharing, and Internet Protocol (TCP/IP) must be active in order for the network to function.
To access the Local Area Connection Properties dialog box, go to the Start menu and click Connect To > Show All Connections, then select Local Area Connections to display the Local Area Connections Properties dialog box. Make sure the appropriate boxes are checked.

## Slide 5: Run the Network Setup Wizard
Windows XP has a Network Setup Wizard that will assist you in setting up a peer-to-peer network.
Notes: To access the Network Setup Wizard:
On the Control Panel, select Network Connections.
In the left pane of the window that displays, under Network Tasks, click “Set up a home or small office network.”

## Slide 6: How do the computers connect to the Internet?
Select the option that most closely describes how your computer connects to the Internet. (If your computer does not have Internet access, select Other.)
Notes: Since the purpose of this peer-to-peer network is to allow computers to connect to each other and share files, the connection to the Internet is not important. Select the option that best describes how (and if) the computer you are configuring connects to the Internet.

## Slide 7: Name the computer
Naming the computer allows you to access it from other computers on the network. You must remember which name corresponds to each computer.
Notes: When you configure a computer using the Network Setup Wizard, give the computer a name. Each computer on the network should have a different name.

## Slide 8: Name the network
The workgroup name identifies the peer-to-peer network that you are creating.
Notes: In Windows XP terms, a peer-to-peer network is a workgroup that links two or more computers together. The workgroup name that you specify must be the same for every computer on the network.

## Slide 9: Turn on file and printer sharing
Be sure to turn on file and printer sharing so that you can share files with other computers on the network.
Notes: File and printer sharing enables the computer to share files with other computers on the network. If the “Turn on file and printer sharing” radio button is not checked, the Windows firewall will prevent the network from sharing files.

## Slide 10: Verify that everything is correct
Check that everything is correct (especially that you typed the network name in correctly) before continuing the wizard.
Notes: The Network Setup Wizard gives you a chance to verify that everything is correct before it sets up the network. If any corrections are needed, click Back.

## Slide 11: Wait for the network to configure
The network may take a few minutes to configure.
Notes: The Network Setup Wizard configures the network while you wait.

## Slide 12: Determine if you need a setup disk
Notes: If all of the computers on your network are running Windows XP, you can use the Network Setup Wizard to set up the network on each computer, and you don’t need a setup disk. However, if some computers have a different operating system, you may need to create a network setup disk at this stage if you don’t already have a network setup disk.
If you are running Windows XP on all systems, or if you have a network setup disk, select “Just finish the wizard” and then restart your computer when prompted.
Next, configure the other computers on the network by going through the same procedure as for the first computer.

## Slide 13: Check the details of the connection
Type ipconfig/all at the command prompt to display the details of your connection.
Notes: When all of the computers on your network are configured, type ipconfig/all to view the configuration of your network. The results should help you to resolve any problems.

## Slide 14: Turn off simple file sharing
On your peer-to-peer network, you want to have control over who shares files. The first step is to turn off simple file sharing.
Notes: If you are using Windows XP, turn off simple file sharing so that you can control who views which files:
From the Start menu, click My Computer.
On the Tools menu, click Folder Options.
In the dialog box that appears, select the View tab.
In the Advanced Settings section, make sure “Use simple file sharing” is not selected.

## Slide 15: Configure folders for file sharing
If there are certain folders that you want to share or that you do not want to share on your network, you can indicate the sharing permission from the Properties window.
Notes: To configure file sharing for a folder, right-click the folder and select Properties.
In the Properties box that displays, click the Sharing tab.
To share files, select the “Share this folder” radio button; then supply a name by which the folder can be recognized on the network. You can also enter a maximum number of users allowed to view the file at once.
To set restrictions, select the Permissions tab. In the box that displays, click Add to find users or groups with whom to share files, or click Remove to select a group you do not want to share files with.
For each group, you can assign varying levels of permissions. These function as variations on the following:
Read Only: You want your friend to read a poem you wrote but not to make any changes to your work.
Write/Change: You want a friend to help edit your essay but you don’t want her deleting it.
Full Access: Your friend wrote an essay on your laptop computer, so now you want to share it with him and grant him full access to make changes or delete it.

## Slide 16: Access shared content from My Network Places
To access shared content from other computers on the network, open the My Network Places folder from the Start menu.
Notes: From My Network Places, click the Shared Docs folder to access shared files.